## Slide 1: Hardware-Software Co-Design for Accelerating the Image Searching Program “Find Face”
資訊工程學系 梁智湧

## Slide 2: Background
This is the final project of the course “Introduction to Hardware-Software Codesign and Implementation”
Students are given a sample program “Find Face”, which is written in C.
The goal of the project is to accelerate the program as much as possible, with techniques including hardware-software codesign.
Notes: 這個Project是軟硬體協同設計概論與實作的期末專題
老師給了學生Find Face這支用C寫的程式
目標就是要以軟硬體協同設計的方式盡可能地加速這支程式

## Slide 3: Environment – Experiment Board
ZedBoard
  Xilinx Zynq-7020 APD
    2 ARM Cortex A9’s @ 667MHz
    FPGA block @ 100MHz
    512MB DDR3 DRAM
    Integrated UART, SD, USB, and Ethernet controller
    AXI4 are used for IP integration
Notes: 這是我們在實驗室中使用的板子
上面有CPU也有FPGA
並有互相構通的interface

## Slide 4: Environment – Development Tool
Xilinx EDA Tools
  Hardware design IDE:
    Xilinx Platform Studio (XPS)
  Software development IDE:
    ISE Software Development Kit (SDK)
Notes: 開發上使用的是Xilinx EDA Tools
硬體我們寫Verilog
軟體則是C

## Slide 5: Find Face – Goal
To find a specified face from a picture with a group of faces.
Group picture (1920 x 1080 pixels)
Target picture (32 x 32 pixels)
Notes: 現在介紹Find Face這支程式
他的功能其實就是在一張大圖中(稱為group picture)
找到一張臉(稱為target picture)

## Slide 6: Find Face – Solution
Read 2 images
  Group
  Target
Perform median filtering
  2D median filtering using a 3x3 window
Find the face (match)
  Iterate the group picture.
  Calculate SAD for each region and target picture.
    (Sum of Absolute Difference)
  Find smallest SAD  answer.
Notes: 這支程式的作法
在前面有些準備工作
重點在第三個部分 一個叫做match的function裡
他會搜尋group picture中的每個區域
去計算出他們個別與target picture的SAD
最後有最小SAD的那個區域即為這支程式所認定的答案

## Slide 7: Iterating (match)
Group picture (1920 x 1080 pixels)
32 x 32
Notes: 這邊用圖示意
程式會搜尋group picture每個32*32的區域

## Slide 8: SAD – Sum of Absolute Difference
Get absolute difference of each pixel.
Sum these absolute differences.
Target picture
32 x 32
Iterated region
32 x 32
Notes: 在每個被搜尋的區域
總共有32*32也就是1024個pixel
以這些pixel計算出這個區域的SAD
在軟體的作法上也就是這支程式原先的作法上
也只能去iterate這1024個pixel

## Slide 9: Problem on Pure-Software
By behavior profiling, the hotspot of the program is on SAD calculation.
There are too many loop iterations.
  Which are done sequentially.
Notes: 我們根據對這支程式profile的結果可以得知
這支程式最慢的部分就是SAD的計算
原因是太多loop iteration了

## Slide 10: Solution by Hardware-Software Codesign
Implement SAD calculation in hardware and parallelize this portion.
  Get absolute differences of all pixels in one cycle.
  Sum all of them.
    To meet the timing constraint, this has to be done in 5 clock cycles.
Notes: 那最直覺的加速辦法當然就是把這個SAD的計算過程在硬體中完成
硬體因為其平行運算的特質
可以在一個cycle內算完所有pixel的absolute difference
接著只要把這些值加起來就好了
不過因為一次做這麼多的加法propagation delay會太久
所以要分成5個cycle來加
也就是我們將這個部分移到硬體後
原先軟體要iterate 1024次的計算現在只需要5個clock cycle就能完成

## Slide 11: Problems & Solutions (1/4)
Memory communication slows down the execution.
  Implement whole “match” in hardware.
    Migrate flow control from software to hardware.
    Read pixel data in hardware.
Notes: 但是這樣的設計並非完美
仍有其他問題影響著加速的效率
接著說明一下其他加速的概念
第一個就是
軟體與硬體之間靠memory溝通
也就是太多的溝通就會讓整支程式快不起來
所以這邊乾脆一點 我們把整個match都搬到硬體去
所有的flow control都在硬體完成
並且直接由硬體從memory讀取圖片的pixel資料

## Slide 12: Problems & Solutions (2/4)
For SAD computation, all pixel data must be stored in distributed RAM, which is resource (LUT) consuming.
Only two 32 x 32 dRAM can be constructed to store pixels of the target and the region of the group that are immediately calculated.
Reading pixels from memory is also slow.
  Improve the utilization of group data.
    Read each pixel in group picture only once.
    With help of BRAM (block RAM)
Notes: 第二個問題就是
因為我們在計算SAD時 是直接開32*32byte的distributed RAM來儲存計算的pixel
但這樣開非常耗硬體resource 在我們resource有限的情況下 也沒辦法再開更大的distributed RAM了
可是 從memory讀取pixel出來是相對較慢的
我們希望能夠每個pixel就只被從memory抓出來一次
因次我們這邊使用Block RAM來改進pixel資料的使用效率
Block RAM是硬體中一個特化的資源
雖然每次存取都需要一個cycle來完成
但對於存放較大量的資料可以省下大量的硬體resource

## Slide 13
Memory
32 1920-byte BRAMs
Load
Notes: 我們使用了32個1920byte長的block RAM
一開始先從memory load出group picture的前32個row
一個row一個row的讀出來 存在這些block RAM中

## Slide 14
32 1920-byte BRAMs
Shift load column by column
32 x 32 dRAM
for some region of group picture
Fill the dRAM (shift 32 times).
Calculate SAD & shift.
Notes: 因為剛剛說過 SAD計算需要資料是存在distributed RAM中
所以我們一個column一個column的把資料shift到distributed RAM中
一開始我們就一直shift 直到塞滿32*32pixel
塞滿以後就可以開始算SAD
算完以後就再shift
就這樣重複直到整個row的做完
由於我們有效保留了許多pixel的資料
因此我們也不用一直重複load到同樣的pixel
在這邊就省掉了一些時間

## Slide 15: Problems & Solutions (3,4/4)
Each SAD calculation requires 5 clock cycles to complete
  Compute SAD in pipeline style.
    Amortized 1 cycle for each SAD.
The SAD calculation stops to wait for loading next row.
  Loading next row while computing SAD.
    Use one more BRAM
Notes: 第三個就是 剛剛說SAD計算需要5個cycle來完成
但就把他pipeline化後
平均每個SAD其實只需要1個cycle就可以算出來
最後一個就是
我們盡量讓SAD的計算與memory的loading都不要idle
因此在計算SAD的同時繼續去load下一個row

## Slide 16: Result
After the acceleration with hardware-software codesign:
  The result of the program:
    Same as the original one before acceleration.
  The execution time: 80ms
    Originally 32 seconds. (400 times faster)
    Fastest in the course.
Notes: 以上大致上是我在這個專題中所使用的加速方式
那執行的結果是與加速前相符的
而時間則是從32秒進步到了80毫秒
也是全班最快的的加速成果

## Slide 17: Conclusion
Hardware: 100MHz, Software: 667MHz.
  Although the hardware has a lower clock rate, it still has the performance much better than the software.
Either the software or the hardware has jobs that are more suitable than the other, and both have the advantages doing its jobs.
  For example,
    Hardware: better performance & better parallel computation
    Software: better flexibility & better development efficiency
  The goal of hardware-software co-design is to take these benefits on developing programs.
Notes: 最後做個結論
我覺得這個專題還蠻有趣的就是
我們可以看到軟體的CPU是667MHz
但硬體僅有100MHz卻能夠在效能上遠遠超過軟體
不過也不是說什麼都用硬體寫就一定比較好
而是軟體與硬體各有其好處
因此應該是要根據程式的各個部分所需
選擇較有利的方式去協同設計

## Slide 18: Thank You

## Slide 19: Q & A